## Slide 1: Practice: Logisim Ⅱ (Week 4)

## Slide 2: Edit appearance
You can edit circuit’s subcircuit appearance

## Slide 3: Labeling
You should label for every inputs & outputs

## Slide 4: Clock
Add a clock
  You can enable the clock and change the clock frequency

## Slide 5: Clock
Test a D flip-flop with a clock
  Rising edge & falling edge

## Slide 6: Tristate Buffer
Controlled buffer in Logisim
  When E = 1, the output O follows the input D
  When E = 0, the output O is in Hi-Z

## Slide 7: Logging
You can check the previous input & output by using the logging module

## Slide 8: Logging
The ‘Table’ tab shows the previous input and corresponding output of the circuit
Also, you can save them to a file

## Slide 9: Practice

## Slide 10: Practice 1
Make a 4bit Shifter
  You can use built-in 4-to-1 Multiplexer
  refer to lecture note 03
Notes: Next chapter, Ealier Technology, will be helpful to understand SASMvm more easily.

## Slide 11: Practice 2
Make a 1bit Register
  You can use built-in D-flip-flops & Multiplexer
Make a 4bit Register
  You have to use 1bit Register you made
Notes: Next chapter, Ealier Technology, will be helpful to understand SASMvm more easily.

## Slide 12: Practice 3
Make a 2-to-1 multiplexer using tristate buffer

## Slide 13: Practice 4
Make a Memory Cell
  You can use 1 And gate, 1 D flip-flop, 1 Tristate buffer
Make a 4x4 RAM
  you have to use memory cell you made

## Slide 14: Practice submission
오후 11시까지 각 Practice 파일을 dccpta@aces.snu.ac.kr 로 제출
  0403_이름_practice(번호).circ의 형식으로 총 4개의 파일을 제출
  파일명 다를 경우 무효처리
과제 미제출시 실습수업 결석
Notes: Next chapter, Ealier Technology, will be helpful to understand SASMvm more easily.