## Slide 1: Lab. 09
Logic Design Lab.
Spring 2014
Prof. Naehyuck Chang
(naehyuck@snu.ac.kr)
TA. Taeyoung Kim
(tykim@iris.snu.ac.kr)
TA. Duseok Kang
(kangds0829@iris.snu.ac.kr)

## Slide 2: Practice (Result Report)
Implement a 5-input, one cathode 7-segment display output logic as below using 16:1 MUX and any other logic gates we have learned in previous lectures
  Input
  - Two 2-bit binary inputs (00,01,10,11), One 1-bit selector input
  Output (7 segment display)
    Case1 (when adder is selected) :
    - “A1A0 + B1B0” result in 7 segment decimal output (“0” ~ “6”)
    Case 2 (when comparator is selected) :
    - If A1A0 >= B1B0, then 7 segment decimal output “1”
    - If A1A0 < B1B0, then 7 segment decimal output “0”
    Write result report (9th) about today’s practice. Maximum 3 pages. (Due : April, 9st)
A1
A0
B1
B0
S
?