## Slide 1: Lab. 15
Logic Design Lab.
Spring 2014
Prof. Naehyuck Chang
(naehyuck@snu.ac.kr)
TA. Taeyoung Kim
(tykim@iris.snu.ac.kr)
TA. Duseok Kang
(kangds0829@iris.snu.ac.kr)

## Slide 2: Example

## Slide 3: Example
CPLD
Status
Score
Start
Reset

## Slide 4: Example
CPLD
Status
Score
Start
Reset

## Slide 5: CPLD (Complex Programmable Logic Device)
CPLD (Xilinx XC9536)
Xilinx XC9536XL
  5ns pin-to-pin logic delays
  System frequency up to 178MHz
  36 macro cells with 800 usable gates
  Optimized for high-performance 3.3V systems
    5V tolerant I/O pins accept 5V, 3.3V, and 2.5V signals
    3.3V or 2.5V output capability

## Slide 6: CPLD (Complex Programmable Logic Device)
PLCC44 Socket Image & Pin Assignment (Bottom view)
You can insert CPLD to your circuit with PLCC44 socket.
There are 44 pins at 9536 CPLD and PLCC44 socket.

## Slide 7: CPLD (Complex Programmable Logic Device)
Implement Design
Simulation
Floorplan IO – Pre-Synthesis
  - Modify UCF file
Manage Configuration Project
  Open .jed file
  Erase
  Program

## Slide 8: CPLD (Complex Programmable Logic Device)
9536 Pin Assignment
There are 3 VCCs and 3 GNDs.
TCK, TDI, TDO, TMS are used for reprogramming circuit to 9536.
You can use PIN5 as global clock.

## Slide 9: CPLD (Complex Programmable Logic Device)

## Slide 10: CPLD (Complex Programmable Logic Device)

## Slide 11: Practice
Implement the “2:4 Decoder” on an universal board
  Use CPLD
  Input : 2 switches
  Output : 4 LEDs
  Write VHDL or Verilog code for the decoder
  Simulate and verify